## Slide 1: Harvesting Rare Isotopes at NSCL and FRIB
Greg Severin
HRS 2018

## Slide 2: Outline
Radiotracing– the concept, and examples.
How NSCL and FRIB expand the radiotracing palette
An example for harvesting: 47Sc
Outlook

## Slide 3: Radiotracing, and the Tracer Principle
George de Hevesy
The Nobel Prize in Chemistry 1943 was awarded to George de Hevesy "for his work on the use of isotopes as tracers in the study of chemical processes".
?

## Slide 4: Water flow in the ocean
Nuclear processing plants in Sellafield and La Haugue “salt” the ocean with 99gTc (t1/2= 211,100 y)
Concentrations of 99gTc are measured in the northern seas and compared to discharge data to determine ocean currents
Shi, K, et al Estuarine, Coastal and Shelf Science 127 (2013) 24e28
Orre, S, et al Journal of Marine Systems
Volume 68, Issues 1–2, November 2007, Pages 24–38

## Slide 5: Water flow in the brain
Nature Medicine 5, 1113 - 1116 (1999) doi:10.1038/13427Mental illness and the sciences of brain and behavior
Seymour S. Kety
Short-lived 15O labeled water shows how blood flow changes in the brain under different stimuli.

## Slide 6: sugar and metabolism
Remission
Before Chemotherapy
After Chemotherapy
Molecular imaging of tumor metabolism and apoptosis U Haberkorn, A Markert, W Mier, V Askoxylakis and A Altmann Oncogene (2011) 30, 4141–4151
[18F]FDG

## Slide 7: ImmunoPET: engineered antibodies find aggressive metastatic cancer cells!
89Zr
Yang, D., Severin, G., Dougherty, C., Lombardi, R., Chen, D., Van Dort, M., Barnhart, T., Ross, B., Mazar, A., & Hong, H. (2016). Antibody-based PET of uPA/uPAR signaling with broad applicability for cancer imaging. Oncotarget, 7(45), 73912-73924.

## Slide 8: Now we can learn about almost anything
How does global climate change affect ocean currents?
What parts of the brain are involved with language processing?
Which parts of our bodies are most metabolically active?
  How can we identify disease in the body?
Etc. etc. , and with only a few isotopes.
More radionuclides are needed to expand tracing capabilities, and other applications

## Slide 9: Some useful radionuclides are hard to make
47Sc, 76Br, 67Cu, 28Mg, 211Rn, 229Pa etc.
For example 47Sc: for targeted therapy with radioactive antibodies.
  47Sc’s low energy beta emissions give an appropriate dose to small metastases
  ATN-291 targets cells that are forming metastases
47Sc

## Slide 10: How do we make tracer radionuclides?
Normally: Small proton-only cyclotrons
(are very good at p,n reactions, for example to make 45Ti from 45Sc)

## Slide 11: 45Ti Production at a small cyclotron
22mg Sc foil, 250µm
Water In
Water out
Silver backing
Cyclotron beamport
H+
(Cyclotron)

## Slide 12
45Ti is easy to make, 47Sc isn’t
-N
P
-N
P
+N
Beta-
NSCL
At NSCL, 47Ca is being produced, abundantly, (and is left to decay) every time 48Ca beams are run!!

## Slide 13: Harvesting at NSCL

## Slide 14
229Pa - EDM
44Ti - Astrophysics
134Ce – PET/MR
76Kr/76Br- PET halogenation
47Sc - radioimmunotherapy
Use the whole buffalo
132Sn – Fast Beam

## Slide 15: Beam Blocker (credit Dave M, Patrick G, etc): Rebuild using Titanium (to match FRIB beamstop material)
Beam blocker pictures
Water in
Water out
Water in
Water out
Beam hits here

## Slide 16: Cooling Water Harvesting
Heat Exchange
Gas/Liquid Separator
Ion Exchange
Pump

## Slide 17
Warm, Contaminated
Degassed
Deionized
Cool
Beam

## Slide 18: 48Ca beam (75pnA), one day on, one day off
element | isotope | Activity (mCi)
K | 43 | 8.820
Ca | 47 | 8.433
K | 42 | 5.645
Na | 24 | 1.794
Sc | 47 | 1.393
Be | 7 | 1.287
P | 32 | 1.139
Sc | 48 | 0.928
P | 33 | 0.629
Sc | 44 | 0.600
Sc | 44m | 0.566
Mg | 28 | 0.481
Ca | 45 | 0.157
Sc | 46 | 0.061
Si | 31 | 0.017
Sc | 43 | 0.012
S | 38 | 0.009
Na | 22 | 0.006
Ni | 57 | 0.004
V | 48 | 0.003
Cr | 51 | 0.002
Mn | 52 | 0.002
(I want 47Sc for radioimmunotherapy)
Can’t harvest 47Sc, it’s contaminated with 48Sc! (et al)
Co-collected, but do not generate contaminating radiometals

## Slide 19
Collect on ion exchange beds, separate by ion exchange “chromatography”.
(i.e. exploit differences in aqueous chemistry of Ca2+ and Sc3+)
Mueller, Vermeulen 2014

## Slide 20: Other plans, NSCL
76Br from 76Kr generator --- medicine, e.g. brominated DHT w/Indiana
52Fe, 44mSc, 90Mo, 48V --- trace metal studies in plants w/MSU plant sciences
48Cr, 88Zr --- stockpile stewardship w/LLNL
Etc. --- each incident beam creates a totally different spectrum of available nuclides.

## Slide 21: Plans for harvesting at FRIB
229Pa and 225Ra for EDM experiments w/Jaideep and ANL
211Rn/211At generator for alpha therapy w/UAB, UW
Radiolanthanides for methylotroph research w/MSU microbio
Radiolanthanides for MRI contrast quantification w/MSU radiology
Etc.

## Slide 22
Harvesting
Group:
Paige Abel & Hannah Clause (grad students)
Nicholas Dronchi (undergrad)
Thanks for the opportunity and for the support!