## Slide 1: Eddy Currents in Accelerator Magnets
Paul Schulman, PHY 862

## Slide 2: Outline
What are eddy currents?
Consequences of eddy currents
  Field modification
  Power loss
Governing equations
  Maxwell’s equations
  Diffusion approach
  Small perturbation approach
Applications
  Yokes
  Coils
  Mechanical structures
  Beam pipes
Minimizing eddy current effects
Wikipedia contributors. "Eddy current." Wikipedia, The Free Encyclopedia. Wikipedia, The Free Encyclopedia, 3 Dec. 2023. Web. 7 Dec. 2023.
Notes: https://www.rosen-group.com/global/company/explore/we-can/technologies/measurement/eddy-current.html

## Slide 3: Eddy Currents
Changing magnetic field induces closed-loop currents in conductors
Induces opposing magnetic field
Lenz’s law
  “The current induced in a circuit due to a change in a magnetic field is directed to oppose the change in flux and to exert a mechanical force which opposes the motion.”
Modifies the net magnetic field
Generates resistive power losses
tec-science, Eddy Current Testing, 2018, https://www.tec-science.com/material-science/material-testing/eddy-current-testing-ect/
Notes: https://www.rosen-group.com/global/company/explore/we-can/technologies/measurement/eddy-current.html

## Slide 4: Field Modification
Lenz’s law
  Opposing magnetic field
Lag
  Must wait for eddy current to disappear
Time and space varying
  Complex to model
Sinha, Gautam, and S. S. Prabhu. "Analytical model for estimation of eddy current and power loss in conducting plate and its application." Physical Review Special Topics-Accelerators and Beams 14.6 (2011): 062401.

## Slide 5: Resistive Power Loss
Heating of magnets
  Bad for superconducting magnets
  Can be damaging to materials
Lorentz’s forces
  Material stresses
Jenner, LJ & Bailey, Ian & Clarke, D & Clarke, Jim & Davies, K & Gallagher, A & Gronberg, J & Hagler, Li & Hesselbach, S. & Nelson, C & Piggott, WT & Rochford, James. (2008). A Study of Mechanical and Magnetic Issues for a Prototype Positron Source Target.

## Slide 6: Governing Equations – Maxwell’s Equations
Quasi-stationary
  Neglecting displacement
No excess charge
Ampere’s law
Faraday’s law
Materials
Wikipedia contributors. "Eddy current." Wikipedia, The Free Encyclopedia. Wikipedia, The Free Encyclopedia, 3 Dec. 2023. Web. 7 Dec. 2023.

## Slide 7: Governing Equations - Diffusion
Lenz’s Law
Magnetic diffusion
Magnetic diffusivity
Current density with vector potential A
Numerical software
  Opera, ROXIE, ANSYS, LS-DYNA
Shafer, R. "Eddy currents, dispersion relations, and transient effects in superconducting magnets." IEEE Transactions on Magnetics 17.1 (1981): 722-725.
Moritz, G., “Eddy currents in accelerator magnets”, 2010, CERN Accelerator School, https://cds.cern.ch/record/1158462/files/cern-2010-004.pdf?version=1

## Slide 8: Governing Equations – Small Perturbations
Ignore the eddy-generated magnetic field
Valid for magnetically thin cases
Geometrically thin
Long, neglect ends
Steady-state conditions

## Slide 9: Eddy Currents in Yokes (2-D Analysis)
Assume a long magnet with a constant packing factor,
Moritz, G., “Eddy currents in accelerator magnets”, 2010, CERN Accelerator School, https://cds.cern.ch/record/1158462/files/cern-2010-004.pdf?version=1
Notes: https://ietresearch.onlinelibrary.wiley.com/doi/full/10.1049/iet-epa.2018.5559

## Slide 10: Eddy Currents in Yokes (3-D Analysis)
Anisotropy of laminated yoke
  Packing factor
  Conductivity
  Permeability
3-D effects arise where:
  Varying packing factor
    Mechanical imperfections
  End regions
    Lack of ‘neighboring’ eddy currents
Moritz, G., “Eddy currents in accelerator magnets”, 2010, CERN Accelerator School, https://cds.cern.ch/record/1158462/files/cern-2010-004.pdf?version=1
2-D
3-D
Notes: https://ietresearch.onlinelibrary.wiley.com/doi/full/10.1049/iet-epa.2018.5559

## Slide 11: Eddy Currents in Coils
Exciting coils
  Rise/fall eddy currents alters current density distribution
  Undesired field distortion
Superconducting coil losses
  Coupling between filaments
  Coupling between cable strands
Wenjie Han, Guanqun Li, Bin Qin, Xu Liu, Dong Li, Qushan Chen, Geng Chen, "Coil induced eddy current analysis of a fast kicker magnet, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment," Volume 1039, 2022, 167151, ISSN 0168-9002, https://doi.org/10.1016/j.nima.2022.167151.
Russenschuck, S., Field Computation for Accelerator Magnets: Analytical and Numerical Methods for Electromagnetic Design and Optimization, 2010, 9783527407699, https://doi.org/10.1002/9783527635467
Notes: https://www.researchgate.net/figure/Eddy-currents-induced-in-a-material-by-an-alternating-current-in-a-coil_fig1_263061139

## Slide 12: Eddy Currents in Mechanical Structures and Beam Pipes
Brackets, collars, shells, etc.
Rods and pins holding laminated sheets together
  Flux loops
  Insulate
  Minimum flux areas
Eddy currents in beam pipes
  Heating of beam pipes
    Add cooling lines, ribbing
      Eddy currents in cooling lines, ribbing
        More losses
Avoid flux loops, electrically insulate
Moritz, G., “Eddy currents in accelerator magnets”, 2010, CERN Accelerator School, https://cds.cern.ch/record/1158462/files/cern-2010-004.pdf?version=1

## Slide 13: Minimizing Eddy Current Effects
Laminated magnets
Increasing the silicon content of iron
Use non-conductive materials when possible
Avoid saturation
  Magnetic end-field region
  Middle of magnet
Chamfered edge instead of sharp edge
Slits
Long magnets over short magnets
Low-loss wire in superconducting coils
Bermúdez, Alfredo, Dolores Gómez, and Pilar Salgado. "Eddy-current losses in laminated cores and the computation of an equivalent conductivity." IEEE Transactions on magnetics 44.12 (2008): 4730-4738.
Fischer, Egbert, et al. "3-D transient process calculations for fast cycling superferric accelerator magnets." IEEE transactions on applied superconductivity 16.2 (2006): 407-410.

## Slide 14: References
Moritz, G., “Eddy currents in accelerator magnets”, 2010, CERN Accelerator School, https://cds.cern.ch/record/1158462/files/cern-2010-004.pdf?version=1
Bertotti, Giorgio. "Physical interpretation of eddy current losses in ferromagnetic materials. I. Theoretical considerations." Journal of applied Physics 57.6 (1985): 2110-2117.
Nan, Xi, and Charles R. Sullivan. "Simplified high-accuracy calculation of eddy-current loss in round-wire windings." 2004 IEEE 35th Annual Power Electronics Specialists Conference (IEEE Cat. No. 04CH37551). Vol. 2. IEEE, 2004.
Fischer, Egbert, et al. "3-D transient process calculations for fast cycling superferric accelerator magnets." IEEE transactions on applied superconductivity 16.2 (2006): 407-410.
Sinha, Gautam, and S. S. Prabhu. "Analytical model for estimation of eddy current and power loss in conducting plate and its application." Physical Review Special Topics-Accelerators and Beams 14.6 (2011): 062401.
Kim, A. A., et al. "Energy loss due to eddy current in linear transformer driver cores." Physical Review Special Topics-Accelerators and Beams 13.7 (2010): 070401.
Jenner, LJ & Bailey, Ian & Clarke, D & Clarke, Jim & Davies, K & Gallagher, A & Gronberg, J & Hagler, Li & Hesselbach, S. & Nelson, C & Piggott, WT & Rochford, James. (2008). A Study of Mechanical and Magnetic Issues for a Prototype Positron Source Target.
Ammari, H., et al. “A Justification of Eddy Currents Model for the Maxwell Equations.” SIAM Journal on Applied Mathematics, vol. 60, no. 5, 2000, pp. 1805–23. JSTOR, http://www.jstor.org/stable/3061711. Accessed 7 Dec. 2023.
Wikipedia contributors. "Eddy current." Wikipedia, The Free Encyclopedia. Wikipedia, The Free Encyclopedia, 3 Dec. 2023. Web. 7 Dec. 2023.
Bordry, F. et al. (2020). Accelerator Engineering and Technology: Accelerator Technology. In: Myers, S., Schopper, H. (eds) Particle Physics Reference Library . Springer, Cham. https://doi.org/10.1007/978-3-030-34245-6_8
Wenjie Han, Guanqun Li, Bin Qin, Xu Liu, Dong Li, Qushan Chen, Geng Chen, "Coil induced eddy current analysis of a fast kicker magnet, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment," Volume 1039, 2022, 167151, ISSN 0168-9002, https://doi.org/10.1016/j.nima.2022.167151.
Russenschuck, S., Field Computation for Accelerator Magnets: Analytical and Numerical Methods for Electromagnetic Design and Optimization, 2010, 9783527407699, https://doi.org/10.1002/9783527635467
Shafer, R. "Eddy currents, dispersion relations, and transient effects in superconducting magnets." IEEE Transactions on Magnetics 17.1 (1981): 722-725.
Bermúdez, Alfredo, Dolores Gómez, and Pilar Salgado. "Eddy-current losses in laminated cores and the computation of an equivalent conductivity." IEEE Transactions on magnetics 44.12 (2008): 4730-4738.

## Slide 15: Questions?