## Slide 1: Radio Frequency Quadrupoles
Xxxxxx

## Slide 2: What are RFQs
Focuses, accelerates, and Bunches a beam
  Heavy ion, proton beams
  0.01c – 0.06c
  Often one of the first elements a beam encounters
    Initial acceleration affects performance of the entire accelerator
  Bunches adiabatically

## Slide 3: Geometry
Four vanes run the length of the RFQ
  Does not have perfect quadrupole symmetry
  “ripples” are offset by
  Need asymmetry to achieve axial potential difference for acceleration
  RFQ are typically 1 to 3 meters long

## Slide 5: Potential and Electric Field
The Electric field is the primary source of focusing and acceleration
  Influence of magnetic field is velocity dependent
  Geometry of the vanes shape the field
  provides acceleration
  and focus
Where
Quadrupole Focusing
Transverse RF Defocusing
A – Acceleration efficiency
X – Focusing Efficiency

## Slide 6: Adiabatic Bunching in the RFQ
Typically bunching is done in RF cavity before the linac
  RF fields applied to unbunched beam giving varying accelerations
  After a drift the particles are bunched
  Comparatively poor efficiency and beam quality to RFQ bunching
  Increased beam density and space charge
RFQ bunching reduces issues typical of RF bunching
  Low injection energy (typically 50-100 keV), initial
  increases gradually along RFQ as beam accelerate

## Slide 7: Stages of an RFQ
Radial Matching Section (RM)
  “Ease” beam into time dependent field
  Not needed if the beam is bunched externally
Shaper Section
Gentle Buncher Section
  Where adiabatic bunching occurs
Accelerator Section
  Where primary acceleration occurs

## Slide 8: Transition Cells
Vane pairs that are the same distance from the center at the end can cause problems
  Time-varying on-axis potential
  Variation in output beam energy, asymmetric output beam
Transition cell used after final accelerating cells
  Modulation to no modulation (quadrupole symmetry)
    Same exit parameters as a regular quadrupole
  Parameters chosen so that potential and electric field are continuous
  Vane tips slightly extended to help with matching

## Slide 9: QRF at MSU
Four-Rod RFQ as opposed to Four-Vane RFQ
  Used at low frequency (<200 MHz)
  Rods of varying diameter instead of vanes
  Current comes through “inductive stems”, or charged support structures
  Higher current density than Four-Vane RFQ
  Very compact
    Outer walls have low affect on beam
  At high frequency, rods become difficult to cool

## Slide 10: References
[1] Wangler, T. (2008) RF Linear Accelerators 2nd Edition. Wiley-VCH. ISBN 3527406808
[2] Lombardi, A. (2006) The Radio Frequency Quadrupole. DOI: 10.5170/CERN-2006-012.201
[3] Kester, et al. (2010). ReA3 – The Rare Isotope Reaccelerator at MSU. Aproceedings – 25th Linear Accelerator Conference LINAC 2010
[4] Vretenar, M. (2009) The Radio Frequency Quadrupole. CAS Darmstadt 2009. URL: http://toddsatogata.net/2019-USPAS/Handouts/Vretenar-RFQ.pdf